## Slide 1
Jung Me Park, Ph.D
    ECE Department, Kettering University
    jpark@kettering.edu
CE320 : Microcomputers I
Lecture 13: Stack Operation

## Slide 2: Today’s Lecture Outline
What is the STACK
  The STACK and the STACK Pointer
STACK Operations
  PUSH and PULL
Example Codes
Main Uses of the STACK

## Slide 3: What is the STACK (I)
The stack is a section of RAM used for temporary storage
  A stack is a range of consecutive memory locations set aside for temporarily storing and retrieving data bytes.
Stacks behave much like books stacked on a table.
  The data structure of the STACK is Last In First Out (LIFO):
    The last item added to the Stack is the first item used.
Notes: Stack is a section of the memory reserved for special
use.
- Elements can be accessed (read/write) from only its top

## Slide 4: What is the STACK (II)
The STACK is an array of memory dedicated to temporary storage.
A section of regular RAM (stack space) that all programs agree will be used for nothing else.
Standard convention is that the stack grows towards lower addresses when data is added.
$3400
Last item placed
onto the stack
First item placed
onto the stack
First item that can be removed from the stack
Last item that can be removed from the stack
Top of stack
Bottom of stack
$35FF
Used stack
space
Available
stack
space

## Slide 5: The STACK (HCS12)
The STACK is used
  To keep track of a program's internal operations including functions, return addresses, passed parameters, etc.
  When you use subroutines and interrupts it will be essential to have such a storage region.
HCS12 stack grows from a high address toward lower addresses and has a 16-bit stack pointer (SP) that points to the top byte of the stack.
  When an item is added to the top of the STACK, the stack grows toward lower addresses
Bottom element
Top element
$3600
$35FF
$35FE
$35FD
$35BF
$35FB
$35FA
$35F9
High Address
Low Address
SP

## Slide 6: The Stack Pointer
The programmer gets to decide where in RAM the stack is located.
  This can be done by setting the value in the stack pointer register (SP).
  Usually the address started from the highest RAM address, plus one : $3FFF +1. For us, that address is $4000.
  In many programs, one of the first instructions will be the stack point initialization.
  LDS # $3FFF +1.

## Slide 7: The Stack Pointer
The Stack Pointer (SP) register is used to indicate the location of the top of the stack.
SP is Initialized ONCE before the first use
  LDS #<address> : Load the stack pointer
    Use only immediate addressing mode.
SP decreases when you put an item on the stack
SP increases when you pull the item from the stack
PUSH
POP
$3600
$35FF
$35FE
$35FD
$35FC
$35FB
$35FA
$35F9
SP
Ex: LDS #$3600

## Slide 8: STACK Operations : PUSH and PULL
Stack operations are grouped into two types, Pull and Push, which correspond to Load and Store.
The HCS12 provides instructions for pushing and pulling all CPU registers except the stack pointer.
  Push : copy data from a register to the memory addressed by SP.
    Prior to writing to memory, SP is automatically decremented.
  Pull : copy data from the memory addressed by SP into a register.
    After the data is copied, SP is automatically incremented.
PUSH
POP
$3600
$35FF
$35FE
$35FD
$35FC
$35FB
$35FA
$35F9
SP

## Slide 9: STACK Operations : PUSH
Push (or Store ) an item to the STACK
  Decrement the Stack Point
  Copy the data from the register to the STACK
  No affect on CCR bits
Six PUSH instructions:
Page 9
Assembly | Meaning | Operation
PSHA
PuSH Accumulator A onto Stack
SP=SP-1
PSHB
PuSH Accumulator B onto Stack
SP=SP-1,
PSHC
PuSH CCR onto Stack
SP=SP-1,
PSHD
PuSH D register onto Stack
SP=SP-2,
PSHX
PuSH X register onto Stack
SP=SP-2
PSHY
PuSH Y register onto Stack
SP=SP-2, Mem[SP:SP+1] =Y
, then copy A to Mem[SP]
then copy B to Mem[SP]
copy CCR to Mem[SP]
Mem[SP: SP+1] =D
, Mem[SP: SP+1] =X
Notes: Huang, Han-Way. The HCS12 / 9S12: An Introduction to Software and Hardware Interfacing (Page 147). Cengage Textbook. Kindle Edition.

## Slide 10: STACK Operations : PULL
Pull (or Pop ) an item from the stack
  Load data from the top of the STACK to a register
  Then, increment the Stack Pointer
  No affect on CCR bits
Six PULL instructions:
Assembly | Meaning | Operation
PULA
PULl Accumulator A from Stack
A=Mem[SP] then SP=SP +1
PULB
PULl Accumulator B from Stack
B=Mem[SP] then SP=SP +1
PULC
PULl CCR from Stack
CCR=Mem[SP] then SP=SP +1
PULD
PULl D register from Stack
D=Mem[SP: SP+1] then SP=SP +2
PULX
PULl X register from Stack
PULY
PULl Y register from Stack
Y=Mem[SP: SP+1] then SP=SP +2
X=Mem[SP: SP+1]then SP=SP +2
Notes: none
Huang, Han-Way. The HCS12 / 9S12: An Introduction to Software and Hardware Interfacing (Page 147). Cengage Textbook. Kindle Edition.

## Slide 11: The STACK (HCS12)
The memory space available for use by the stack is limited in a computer system. There is always a danger of stack overflow and stack underflow.
Stack overflow is a situation in which the processor pushes data into the stack too many times so that the SP points to a location outside the area allocated to the stack.
Stack underflow is a situation in which the processor pulls data from the stack too many times so that the SP points to an area below the stack bottom.
If you push or pull too many, the processor writes in locations outside the area allocated to the stack
  The program may crash because you mistakenly write in the area of the data or the program
  It is the programmer responsibility to keep the SP within the stack area
3FFF
Bottom element
3400
Top element
Available
Area
SP
Used
Area
Notes: A stack overflow is an undesirable condition in which a particular computer program tries to use more memory space than the call stack has available.
Be sure to locate the top of the stack far away from the location of your code and data. Otherwise your code and data may be wiped out by stack operations.

## Slide 12: Example Codes : Example 1
Data Exchange: Swap
1: LDS #$3600
$3600
$35FF
SP
2: LDAA #$20
SP:
3: PSHA
4: LDAB #$28
5: PSHB
$3600
A:
$20
$35FE
$35FC
$35FF
$35FB
B:
$28
$35FE
$20
$28
6: PULA
7: PULB

## Slide 13: Example Codes : Example 1
cont.
1: LDS #$3600
$3600
$35FF
2: LDAA #$20
SP:
3: PSHA
4: LDAB #40
5: PSHB
A:
$20
$20
$35FE
$35FC
$35FB
B:
$28
$35FE
SP
$28
6: PULA
$35FF
7: PULB
$3600

## Slide 14: Stack Example #2:
1: LDS #$3600
$3600
$35FF
SP
2: LDAA #0
SP:
3: PSHA
4: LDAA #$20
5: PSHA
$3600
$35FE
$35FC
$35FB
$35FF
$35FE
6: LDD #$012C
7: PSHD
$20
$00
$35FB
$01
$2C
8: PULD
D:
A:
B:
$00
$20
$01
$2C

## Slide 15: Example #3: Draw a stack diagram as you trace these instructions:
1: LDS #$3600
2: LDAA #$AA
3: LDAB #$BB
4: PSHA
5: PSHB
6: PULA
7: PULB
35FD
35FE
35FF
3600
SP
After Line 1
--
A
--
B
$3600
35FD
35FE
35FF
3600
SP
35FD
35FE
35FF
3600
SP
35FD
35FE
35FF
3600
SP
After Line 4
35FD
35FE
35FF
3600
SP
After Line 5
After Line 6
After Line 7
A
B
A
B
A
B
A
B
35FD
35FE
35FF
3600
SP
After Line 3
A
B

## Slide 16: Example #3: Answer
1: LDS #$3600
2: LDAA #$AA
3: LDAB #$BB
4: PSHA
5: PSHB
6: PULA
7: PULB
35FD
35FE
35FF
3600
SP
After Line 1
--
A
--
B
$3600
35FD
35FE
35FF
3600
SP
After Line 3
A
B
$3600
$AA
$BB
35FD
35FE
35FF
3600
SP
After Line 4
A
B
$AA
$BB
35FD
35FE
35FF
3600
SP
After Line 5
A
B
$AA
$BB
$AA
35FD
35FE
35FF
3600
SP
After Line 7
A
B
$BB
35FD
35FE
35FF
3600
SP
After Line 6
A
B
$BB
$AA
$35FF
$AA
$35FE
$BB
$35FF
$BB
$AA
$3600

## Slide 17: Using the Stack Practice
Write contents after each instruction executes:
Instruction | A | B | SP | Mem $3FFD | Mem. $3FFE | Mem. $3FFF
LDS #$4000 | -- | -- | $4000 | -- | -- | --
LDAA #$12 | $12 | -- | $4000 | -- | -- | --
PSHA | $12 | -- | $3FFF | -- | -- | $12
DECA | $11 | -- | $3FFF | -- | -- | $12
LDAB #$34 | $11 | $34 | $3FFF | -- | -- | $12
PSHD | $11 | $34 | $3FFD | $11 | $34 | $12
LDD #$00 | 0 | 0 | $3FFD | $11 | $34 | $12
PULD | $11 | $34 | $3FFF | $11 | $34 | $12
PULA | $12 | $34 | $4000 | $11 | $34 | $12

## Slide 18: Main Uses of the STACK(I)
Saving the Return Address for a Sub-Routine Call:
  Subroutine call instructions save the return address ( address of the instruction immediately following the sub routine call instruction ) in the STACK.
  This is done automatically when the subroutine is called by using JSR (Jump to Subroutine) or BSR (Branch to Subroutine) instruction : will covered more in details next class
      This instruction pushes the address of the instruction immediately following the sub routine call instruction on the top of the stack
  After the subroutine is done executing, it needs to return to the address saved on the stack.
    This is done automatically when you return from the subroutine by using RTS (Return from Subroutine) instruction.
    This instruction pulls the return address from the stack and loads it into the PC.

## Slide 19: Main Uses of the STACK (II)
Temporally Storage for Local Variables:
  A subroutine may need memory locations to hold temporary variables and results. Temporary variables are called local variables because they only exist when the subroutine is entered.
  Local variables are always allocated in the stack so that they are not accessible to any other program units.
Incoming Parameters:
  Incoming Parameters are usually provided as registers. But if we run out of registers, we can always place incoming parameters on the Stack.
  Parameters are pushed into the stack before the subroutine is called. The stack must be cleaned up after the computation is completed.

## Slide 20: Main Uses of the STACK (III)
Saved Registers:
  If we need to use registers inside the subroutine, a good practice is to push the registers’ values at the beginning of the subroutine.
  When the subroutine is finished, the registers recover their original values. This way, the registers are never modified after a subroutine has been executed.

## Slide 21: Summary
STACK
  LIFO
  an array of memory dedicated to temporary storage in RAM
STACK Pointer (SP)
  keep the Address of the top of the STACK
Main operation of STACK
  Push - PSHA, PSHB, PSHC, PSHD, PSHX, PSHY
  Pull - PULA, PULB, PULC,PULD,PULX,PULY
Main uses of the STACK
  Return address after sun-routine call, temporary storage of local variables, incoming parameters, and registers.